## Slide 1: Segurança na IoT Perspectiva geral e o caso SmartThings
Seminário
2019
Nuno Santos

## Slide 2: O que é a Internet of Things (IoT)?
O último grito na evolução da Internet: comunicações machine-to-machine (ou device-to-device)

## Slide 3: Definição de IoT
“Network of physical objects, devices, vehicles, buildings and other items embedded with electronics, software, sensors, and network connectivity that enables these objects to collect and exchange data.”
Wikipedia
“Network of physical objects that contain embedded technology to communicate and sense or interact with their internal states or the external environment.”
Gartner

## Slide 4: Mais definições
“It is a global network of interconnected objects, uniquely identifiable based on a standard communication protocol.”
[CERP-IoT 2010]
“The Internet of Things allows people and things to be connected Anytime, Anyplace, with Anything and Anyone, ideally using Any path/network and Any service.”
[Perera et al. 2014]

## Slide 5: “Coisas” ligadas à Internet

## Slide 6: “Coisas” ligadas a “coisas”
- Complex and heterogeneous
resources and networks

## Slide 7: Pessoas ligadas a “coisas”
Motion sensor
Motion sensor
Motion sensor
ECG sensor
Internet

## Slide 8: “IoT enables de future”

## Slide 9: Tendências da tecnologia

## Slide 10: Proliferação de redes wireless de sensores
Sink
node
Gateway
Core network
e.g. Internet
Gateway
End-user
Computer services
As redes tipicamente envolvem dispositivos de baixo consumo
Consistem em um ou mais sensores, podem ser de diferentes tipos (ou actuadores)

## Slide 11: Ecosistema IoT oferecido por provedor de serviço

## Slide 12: SmartHome: Casa inteligente
Plataformas para SmartHome usam home hubs para interligar smart devices de diferentes fabricantes
Amazon Echo
Google Home
Apple HomeKit
Samsung SmartThings
Notes: Tecnologia emergente que suporta interligação e controlo inteligente de dispositivos e permite que collaborem entre eles

## Slide 13: Duas faces da segurança: safety e segurança
Notes: https://www.ipa.go.jp/files/000053921.pdf

## Slide 14: Problemas de safety: Exemplos de acidentes
Notes: https://www.ipa.go.jp/files/000053921.pdf

## Slide 15: Problemas de security: Exemplos de incidentes
Notes: https://www.ipa.go.jp/files/000053921.pdf

## Slide 16: Outro exemplo de violação de security
Roubo de grandes quantidades de informação devido a infecção de terminais POS por malware
In 2013, it was found that POS terminals of a large retail chain in the U.S. were infected by malware (malicious software), and credit card information of 40 million customers and personal information of 70 million customers were leaked.
Notes: https://www.ipa.go.jp/files/000053921.pdf

## Slide 17: Exemplo onde safety e security são afectados
Pacemakers cardíacos podem ser parados via wireless
In 2012, a U.S. researcher published an experiment, showing that transmission equipment can make cardiac pacemakers deliver a fatal electric current to hearts or falsify software in the pacemakers from a distance of less than 10m.
Notes: https://www.ipa.go.jp/files/000053921.pdf

## Slide 18: O que vamos ver a seguir
Riscos e desafios de segurança em IoT
Segurança na plataforma SmartThings

## Slide 19: Riscos e desafios de segurança em IoT

## Slide 20: Estudo realizado pela IETF
Draft: Security Considerations in the IP-based Internet of Things
Torna-se um IRTF Internet Draft em 2016
  State-of-the-Art and Challenges for the Internet of Things Security
  https://tools.ietf.org/html/draft-irtf-t2trg-iot-seccons-16
Também bom sumário das iniciativas de standardização
Notes: The Internet Research Task Force (IRTF) focuses on longer term research issues related to the Internet while the parallel organization, the Internet Engineering Task Force (IETF), focuses on the shorter term issues of engineering and standards making.
https://irtf.org/

## Slide 21: Dimensões da segurança em IoT
Security
  Confidentiality
  Authentication
  Integrity
  Authorization
  Availability
24h available

## Slide 22: Vulnerabilidades no ciclo de vida das “coisas”
Application Running
Reconfigured
Manufactured
Installed
Commissioned
Application Running
Software update
Removed & replaced
Decommissioned
Reownership & recommissioned
Bootstrapping
Operational
Maintenance & re-bootstrapping
Operational
Maintenance & re-bootstrapping

## Slide 23: Vulnerabilidades no ciclo de vida das “coisas”
Application Running
Reconfigured
Manufactured
Installed
Commissioned
Application Running
Software update
Removed & replaced
Decommissioned
Reownership & recommissioned
Bootstrapping
Operational
Maintenance & re-bootstrapping
Operational
Maintenance & re-bootstrapping

## Slide 24: Ameaças de segurança para as “coisas”
Cloning of things
  Clone firmware, security configurations
  Reverse engineer
  Change functionality/add a backdoor
Manufacturing
Application Running

## Slide 25: Ameaças de segurança para as “coisas”
Malicious substitution of things
  Different device is installed during Installation phase
Installation

## Slide 26: Ameaças de segurança para as “coisas”
Eavesdropping attack
  Security parameters exchanged in clear text
  Device lifetime exceeds the cryptographic algorithms lifetime
  Messages during T2T communication
Application operational
Commissioning
Notes: Comissioning = configuração

## Slide 27: Ameaças de segurança para as “coisas”
Man-in-the-middle attack
  Security parameters update exchanged in clear text
  If device authentication is human-assisted, it may create a weak link
Application operational
Commissioning
Hub
Notes: Comissioning = configuração

## Slide 28: Ameaças de segurança para as “coisas”
Firmware attacks
  During maintenance a new malicious firmware may be updated
  Old firmware may contain security exploits
Software update
Application operational
Notes: Comissioning = configuração

## Slide 29: Ameaças de segurança para as “coisas”
Privilege scalation
  Authentication system flaw
  Low privileged user access higher priority resources
Notes: Comissioning = configuração

## Slide 30: Ameaças de segurança para as “coisas”
Privacy threats
  Infer information based on device profile and messaging patterns
  Also known as second channel attack
Notes: Comissioning = configuração

## Slide 31: Ameaças de segurança para as “coisas”
Denial-of-Service attack
  Physically jamming the network medium
  Constrained devices are more vulnerable
    Resource exhaustion
  Compromised devices used in a Distributed DoS
Notes: Comissioning = configuração

## Slide 32: Desafios para IoT segura
Resource constraints
  Lossy and low-bandwidth communication channels
    Possible DoS exploit, due to losses and retransmissions
  Scarce processing and memory capacity limits the usage of resource expensive cryptographic primitives
    Efforts in more efficient cryptography

## Slide 33: Desafios para IoT segura
End-to-end security, protocol translation, and the role of middleboxes
  Sender to receiver confidentiality and integrity
    Encryption commonly used
    Gateways can’t change or access the data
  Constrained IoT networks uses different protocols that may needs translation at middleboxes
    Middleboxes must access the message being sent (no end-to-end security)
Middlebox
Internet

## Slide 34: Desafios para IoT segura
Solutions for end-to-end security challenge
  Share credentials with middleboxes
  Selectively protecting vital and immutable packet parts within a message, may result in poor performance or poor security
    Encrypt and integrity protect most of the message fields except those parts that a middlebox needs to read or change
  Homomorphic encryption techniques
    Limited to arithmetic operations
    Not many libraries with good support yet

## Slide 35: Desafios para IoT segura
Bootstrapping of a security domain
  Creating a security domain from unassociated IoT devices
  Still an unresolved question
Manufactured
Installed
Commissioned
Bootstrapping

## Slide 36: Desafios para IoT segura
Operational stage challenges
  Group Membership and Security
  Group key solutions can be reused in IoT

## Slide 37: Desafios para IoT segura
Mobility and IP network dynamics
  Expected that things will be attached to different networks during its lifetime (wearable sensors)
Hub1
Hub2

## Slide 38: Desafios para IoT segura
Secure software update and cryptographic agility
  IoT devices are often expected to stay functional for several years and decades
  Unattended operation
  Software updates needed for new functionalities and security vulnerabilities
    No incentive by manufactures
    No source code available
    Manual update
    All the update threats
    Source authentication

## Slide 39: Desafios para IoT segura
Verifying device behavior
  How guarantee e that a device is doing what it claims
  Devices may need to connect to the manufactures server, how can a user tell what data is being sent?
  Challenging
    Devices are not only constrained in resources but also in interface
    Place of deployment will vary
    It’s a open question
Some solutions
  Manufacturer Usage Description (MUD) files [ID-MUD]
    A first step in this direction
    Describes what the device is supposed to the network
    network monitoring service can then alert the user if the device does not behave as expected
Notes: Manufacturer Usage Description (MUD) is an embedded software standard defined by the IETF that allows IoT Device makers to advertise device specifications, including the intended communication patterns for their device when it connects to the network.
https://developer.cisco.com/docs/mud/#!what-is-mud

## Slide 40: Desafios para IoT segura
Testing and bug hunting and vulnerabilities
  It remains an open issue how classic quality assurance and bug testing will adapt to IoT devices
  Also the combination of devices from different vendors may lead to dangerous network configurations
Notes: Manufacturer Usage Description (MUD) is an embedded software standard defined by the IETF that allows IoT Device makers to advertise device specifications, including the intended communication patterns for their device when it connects to the network.
https://developer.cisco.com/docs/mud/#!what-is-mud

## Slide 41: Desafios para IoT segura
Privacy protection
  Second channel attacks
Defined as
  awareness of privacy risks imposed by smart things
  individual control over the collection and processing of personal information
  awareness and control of subsequent use and dissemination of personal information by those entities to any entity outside the subject’s personal control sphere

## Slide 42: Desafios para IoT segura
Threats to user privacy
  Identification - refers to the identification of the users and their objects
  Localization - relates to the capability of locating a user and even tracking them
  Profiling - is about creating a profile of the user and their preferences
  Interaction - occurs when a user has been profiled and a given interaction is preferred (targeted marketing)
  Lifecycle transitions - take place when devices are, for example, sold without properly removing private data
  Inventory attacks - happen if specific information about (smart) objects in possession of a user is disclosed
  Linkage - is about when information of two of more IoT systems is combined so that a broader view on the personal data is created
Still an open issue

## Slide 43: Desafios para IoT segura
Trustworthy IoT operation
  Flaws in the design and implementation of a secure IoT device
    Same built in password for all devices (as Dr. Mosse mentioned about routers)
  Tools to find IoT devices in the Internet
    https://www.shodan.io/

## Slide 44: OWASP IoT top 10 vulnerabilities 2018
I1 Weak Guessable, or Hardcoded Passwords
I2 Insecure Network Services
I3 Insecure Ecosystem Interfaces
I4 Lack of Secure Update Mechanism
I5 Use of Insecure or Outdated Components
I6 Insufficient Privacy Protection
I7 Insecure Data Transfer and Storage
I8 Lack of Device Management
I9 Insecure Default Settings
I10 Lack of Physical Hardening
https://www.owasp.org/images/1/1c/OWASP-IoT-Top-10-2018-final.pdf

## Slide 45: Três problemas sérios na plataforma SmartThings
Como impedir que as aplicações tenham acesso abusivo aos smartdevices dos utilizadores?
Como impedir que as aplicações efectuem acções sem o conhecimento dos utilizadores?
Como impedir que diferentes aplicações interfiram entre si causando resultados inesperados pelos utilizadores?